## Slide 1
FEASIBILITY REVIEW
PWE1 HOSS™-VWP
Modular thermal treatment for hypersaline produced water — evaluated as a potential technology partnership for PDO and Oxy.
Vendor claims unverified — pilot required
PREPARED FOR
PDO / Oxy Evaluation
DATE
August 2026
CONFIDENCE
8 / 10

## Slide 2
CONTENTS
Six parts.
01
The Problem
02
The Technology
03
Why Oman
04
The Commercial Case
05
Risk & What's Unverified
06
Recommendation
PWE1 HOSS™-VWP — Feasibility Review

## Slide 3
01
The Problem

## Slide 4
OPERATIONAL REALITY
Produced water is a cost center
that steam demand could offset.
Mature and heavy-oil fields generate large volumes of hypersaline brine. Disposal is expensive. Thermal recovery needs continuous steam. Today these run as two separate cost lines.
High
Disposal cost per m³ in
hypersaline fields
Continuous
Steam demand in thermal-
recovery operations
Unlinked
These cost centers rarely
share infrastructure today
PWE1 HOSS™-VWP — Feasibility Review

## Slide 5
02
The Technology

## Slide 6
HOSS™-VWP
One modular system,
three recovered outputs.
A closed-loop indirect-heating system that converts difficult produced water into usable field resources rather than waste.
01
Steam
Demineralized, high-vapour-fraction steam for field use or EOR injection.
02
Clean Water
Recovered water suitable for reinjection or controlled discharge.
03
Mineral Solids
Concentrated dried solids for disposal — or feed-specific recovery assessment.
PWE1 HOSS™-VWP — Feasibility Review

## Slide 7
PROCESS
Five stages, indirect heating throughout.
1
Feed Conditioning
Incoming brine is prepared for thermal treatment.
2
Slurry Handling
Controlled management of precipitating salts to limit scaling.
3
Vapour Separation
Steam is extracted and routed for field reuse.
4
Indirect Heating
Waste heat, gas, geothermal, solar thermal, or hybrid input drives the process.
5
Water & Solids Recovery
Clean water is separated; remaining minerals are dried and concentrated.
PWE1 HOSS™-VWP — Feasibility Review

## Slide 8
SPECIFICATIONS
Modular capacity, flexible energy input.
Chart: Package Throughput Range (m³/day)
| Minimum Package | Maximum Package
Capacity (m³/day) | 240 | 1110
≈ 1,500–7,000 bbl/day equivalent
Heating can draw from:
Waste Heat
Waste Gas
Geothermal
Solar Thermal
Hybrid
PWE1 HOSS™-VWP — Feasibility Review

## Slide 9
03
Why Oman

## Slide 10
STRATEGIC FIT
The clearest fit: heavy-oil fields
where disposal and steam demand coexist.
COST
Opex Reduction
Converts a disposal cost center into a steam and water source.
REGULATORY
Compliance Fit
Closed-loop recovery aligns with Oman's treatment-over-discharge posture.
ENERGY
Efficiency Story
Waste-heat and flare-gas capture support efficiency and ESG targets.
PWE1 HOSS™-VWP — Feasibility Review

## Slide 11
04
The Commercial Case

## Slide 12
ILLUSTRATIVE ONLY — FIELD-SPECIFIC MODEL REQUIRED
A 500 m³/day module, modeled conservatively.
$25M
Estimated CAPEX
(module + install)
$440K/yr
Net annual benefit,
waste-heat powered
~57 yrs
Simple payback — highly
sensitive to inputs
Payback improves sharply with higher disposal costs, full steam utilization, or free waste-heat input. This is a placeholder model, not an investment figure.
PWE1 HOSS™-VWP — Feasibility Review

## Slide 13
05
Risk & What's Unverified

## Slide 14
TECHNICAL ASSESSMENT
Credible design, undisclosed performance.
STRENGTHS
Modular — scalable field-by-field, no CAPEX concentration
Indirect heating — lower corrosion, simpler operability
Closed loop — minimal discharge, regulatory friendly
Energy flexible — waste heat reduces fuel exposure
UNDISCLOSED
Energy intensity — no kWh/m³ figure published
Steam spec — vapour fraction, purity not stated
Fouling behavior — no operating/maintenance data
Availability — no MTBF or uptime target
PWE1 HOSS™-VWP — Feasibility Review

## Slide 15
PORTFOLIO VIEW
What could go wrong, what could pay off.
RISK
Performance falls short of claims, eroding ROI
Scaling degrades heat transfer over time
Vendor maturity — no performance guarantees seen
Energy cost volatility if not waste-heat powered
OPPORTUNITY
Immediate disposal-cost avoidance
Steam self-sufficiency for thermal recovery
Modular rollout spreads capital risk
ESG-aligned partnership narrative with Oxy
PWE1 HOSS™-VWP — Feasibility Review

## Slide 16
06
Recommendation

## Slide 17
RECOMMENDATION
Qualified proceed to pilot.
Genuine strategic fit for PDO/Oxy heavy-oil operations — contingent on two conditions before any capital commitment.
CONDITION 01
Independent pilot on representative field water — energy use, steam quality, water recovery, fouling behavior.
CONDITION 02
Written performance guarantees tied to liquidated damages — not currently offered.

## Slide 18
PATH FORWARD
Five tracks, 18–30 weeks to a decision.
Chart: Weeks
| Technical Validation | Commercial & Legal | Field Economics | Execution Readiness | Partnership Structure
Core Estimate | 8 | 6 | 4 | 4 | 4
Extended Range | 4 | 2 | 2 | 2 | 2
Bar length = core estimate + extended range per track (e.g. Technical Validation: 8–12 weeks)
01
Engage PWE
Technical review + guarantee terms
02
Select Pilot Site
High water-cut, thermal-recovery field
03
Independent Engineer
Third-party pilot oversight
04
Run Pilot
2–8 weeks, representative feed
05
Decision Gate
Go / no-go to investment committee

## Slide 19
BOTTOM LINE
8/10
Confidence in the strategic case. Confidence in the technology remains outstanding until PWE's claims are independently verified in a field pilot.
Not an investment recommendation